User Manual
Version 1.3.0 – 20110207

# Overview

This version of the Newhall Simulation Model (NSM) is a direct and enhanced port of the Armand Wambeke GW-BASIC port. The simulation core is an effective 1:1 port of the original model, behaving identically given the same dataset and assumptions. This edition goes further to incorporate additional features, such as soil temperature calculations that models thermal lag behavior, along with annual and summer water balances.

Some deviations from the original BASIC model have been made, primarily through the added enhancements. The soil temperature and thermal lag calculations were ported from a partial C++ port of the NSM. These calculations did not make assumptions on lag phases, and required them to be manually specified for summer and winter. Because the datasets used do not cover enough geological information to determine what the lag phase for a location is, we borrow from assumptions used in the BASIC model for other calculations. For the spring, a lag phase of 21 days is assumed, while a lag phase of 10 days is used for the fall.

Annual and Summer water balances were also added to the BASIC model. These water balances are defined as the sum of precipitation minus the sum of evapotranspiration over a year for one figure, and only three months of the summer for the other. AWB is the end total for the entire 12 month duration a dataset covers, while SWB will cover only the three summer months. The summer months are conditional on the location of the dataset, whether it is in the northern or southern hemisphere. “Summer” is considered July through August for the northern hemisphere, and December through February in the southern hemisphere.

This version of the NSM supports the BASIC version's dataset and export formats, which are CSV and FLX files (CSV input files detailed later in this document). In addition to these files are a new XML file format. This format consists of three segments: metadata, input, and output. Metadata is optional, input is required to process a dataset through the model, and output is generated by the model. An exported XML file still retains the source data used to generate it, and can be opened within the application to process it again. Upon exportation, the input segment of the file will remain mostly unaltered (if you have changed the waterholding capacity, or soil-air relationship properties, these will be changed). The output region will be overwritten. The metadata segment will remain unaltered. The XML file format is detailed later in this document.

This version of NSM is built on top of the Java virtual machine. In order to run it, you must have Java installed on your computer. If Java is installed on your computer, the JAR file should be treated as an executable on your computer. If your computer does not recognize it as such, please install Java, which can be obtained at: http://www.java.com Refer to “Java Setup” for more details.
# Java Setup

Java must be installed on any computers that wish to use this version of NSM. Attempting to launch Newhall by double clicking on the included JAR file can quickly test if you have an appropriate version of Java installed. If Newhall does not launch immediately, follow the following instructions per your operating system.

## MacOS X

Versions of MacOS X 10.1 and later should have at least Java 1.4 or later installed. Newhall requires Java 1.5 or later. To verify your version of Java, open a terminal (located in your Utilities folder inside the Applications folder), and type in java -version at the prompt. Because Apple is responsible for the inclusion of the JVM in MacOS X, if your version is too old, you will need to check for system updates.

Due to Oracle's acquisition of Sun Microsystems, they have changed the licensing terms of outside vendor developed JVMs. At some point in the future (as of February 2011), Apple may no longer be responsible for the inclusion of Java in OS X. Refer to modern documentation as to getting Java installed on OS X if this occurs.

## Solaris

Java is part of a standard install of Solaris. If Newhall will not run on your Solaris machine, please contact your system administrator to setup a Java runtime for your use.

## Linux (Ubuntu, Fedora, Debian, SUSE, etc.)

Most Linux distributions offer Java (in the form of either the OpenJDK or official JVM), either pre-installed or as an entry in their package manager of choice. Refer to your distribution's documentation on how to install software via their package manager, and search for a “JRE” package. Install that, and Java will be available to you. If the JAR will not open with a double-click following installation, you can run the JAR file from the command line. Use the command java -jar Newhall.jar to launch Newhall.

For specific instructions per your distribution, a simple search of “[distro name here] java installation” will generally yield up-to-date instructions for how to accomplish the task. More and more distributions are coming with the OpenJDK preinstalled, which is suitable for running Newhall.

## Windows (2000, XP, Vista, 7)

Java is not included by default with Windows. If the JAR does not execute with a double-click, you will need to install Java. Browse to http://www.java.com/ and follow the instructions to install Java on your computer. When Java is properly installed, the icon for Newhall's JAR file should change, and should now launch with a double-click. You will need to have administrator access to your computer to do this, and if your workstation is managed by your employer, you will need to contact your IT administrators to assist you in installing Java.
# Interface Overview

Above is an example of the Newhall interface with a dataset loaded. The loading was accomplished by selecting “Open Dataset” (Control-O) from the “File” menu, and selecting either an XML or CSV file adhering to either the original BASIC NSM file format, or the newer XML file format. The model runs as soon as the dataset is open. Newhall starts up with no dataset loaded.

The main interface consists of four tabs. “Input” covers the input data to the model. This includes temperature and precipitation data, along with some of the most basic metadata. From here you can specify the waterholding capacity (lower left) along with the parameters for the soil-air relationship with the offset and amplitude (these augment the sine wave, shifting the waveform forward and back, and also diminishing the amplitude). Altering any of these fields will cause the model to rerun instantaneously.

“Calendars” covers the temperature and moisture calendar for the location. The temperature calendar is static and directly related to the monthly temperature values. The moisture calendar is altered by both the dataset and the waterholding capacity. These calendars provide general overviews of the dataset's location given the model inputs.
“Results” shows the conclusions of the model run. This includes evapotranspiration calculations, extended statistics about the location (generally these are summaries of what the calendars have laid out), annual rainfall, and regime determinizations.

“Metadata” includes any extended metadata included in the dataset. For legacy datasets, only the most basic fields are populated, due to the sparse nature of the dataset. XML datasets may have a full compliment of fields in the metadata. Refer to the XML file format documentation later in this document to add and change these values.

The menu bars consist of three menus: “File”, “Options”, and “Help”. “File” contains actions to open datasets, and to exit the application. “Options” includes the action to toggle the unitsystem mode. Newhall starts up in metric mode by default, and can toggle back and forth between metric and english seamlessly. The active unit system is displayed at the bottom-center of the window. Note: Whatever unitsystem mode Newhall is in when you export data, that will be the unit system the exported XML file will be in. The “Help” menu includes the option to view the current version and license information for your current version of the Newhall application.

Two buttons are available at the bottom-right of the window: “Export to XML” and “Export to FLX”. These two buttons export the results of the model to two different file formats. The FLX file format is the legacy output of the BASIC version of the model, denoted by the .FLX file suffix. The XML export is a new format meant to accommodate metadata and extended input and output data in a file format that is both machine-readable and human-readable. The FLX file format does not include the input data used to make it, but the XML file will, as it retains the <INPUT> tag.
# XML Format Units Note

The XML export format does not attach units to measurements, but does specify a unit system. Temperature in metric mode is in Celsius, and Fahrenheit in english. Precipitation in metric is measured in millimeters, and inches in english mode.

Latitude and longitude are stored as decimal degrees. Any number of significant figures is acceptable.

Soil-air temperature offsets are temperature measurements, and are Celsius in metric, and Fahrenheit in english.

Annual and Summer water balances are precipitation measurements, and are inches in english, and millimeters in metric.

Calendars assume a constant 30 day month throughout the year, and a 360 day year. This can be interpolated over a 365.25 day year as needed.
# XML File Format Structure

The XML file format consists of a root <model> tag that contains three children tags: <metadata>, <input>, and <output>. The <metadata> tag is entirely optional, but the <input> tag is required to run a model. The <output> tag is generated when exporting the model results to XML. An example file is detailed below.

(The <notes> tag may have several or no <note> child tags. All other tags may not duplicate children tags. Newhall will only read the first set of children tags if this is the case, but will read all <note> tags.)
## Example File

<?xml version="1.0" encoding="UTF-8"?>
<model>
  <metadata>
    <stninfo>
      <stnname>Renovo</stnname>
      <stnid>PAXXX</stnid>
      <stnelev>201.0</stnelev>
      <stateprov>PA</stateprov>
      <country>USA</country>
    </stninfo>
    <mlra>
      <mlraname>Eastern Allegheny Plateau and Mountains</mlraname>
      <mlraid>127</mlraid>
    </mlra>
    <cntinfo>
      <cntper>
        <firstname>John</firstname>
        <lastname>Doe</lastname>
        <title>Assistant Director</title>
      </cntper>
      <cntorg>CEI, Penn State</cntorg>
      <cntaddr>
        <address>123 Fake Address</address>
        <city>Cityopolis</city>
        <stateprov>PA</stateprov>
        <postal>16802</postal>
        <country>USA</country>
      </cntaddr>
      <cntemail>example@nowhere.org</cntemail>
      <cntphone>555-555-5555</cntphone>
    </cntinfo>
    <notes>
      <note>This is a sample NSM file.</note>
      <note>This is another note in the file.</note>
    </notes>
    <rundate>20110207</rundate>
    <nsmver>1.3.0</nsmver>
    <unitsys>metric</unitsys>
  </metadata>
  <input>
    <location>
      <lat>41.3166</lat>
      <lon>-77.7166</lon>
      <usercoordfmt>DD</usercoordfmt>
    </location>
    <recordpd>
      <pdtype>normal</pdtype>
      <pdbegin>1971</pdbegin>
      <pdend>2000</pdend>
    </recordpd>
    <precips>
      <precip id="Jan">59.2</precip>
      <precip id="Feb">61.7</precip>
      <precip id="Mar">79.8</precip>
      <precip id="Apr">83.3</precip>
      <precip id="May">84.8</precip>
      <precip id="Jun">124.0</precip>
      <precip id="Jul">91.2</precip>
      <precip id="Aug">87.1</precip>
      <precip id="Sep">95.8</precip>
      <precip id="Oct">73.7</precip>
      <precip id="Nov">88.6</precip>
      <precip id="Dec">88.6</precip>
    </precips>
    <airtemps>
      <airtemp id="Jan">-3.3</airtemp>
      <airtemp id="Feb">-2.0</airtemp>
      <airtemp id="Mar">3.1</airtemp>
      <airtemp id="Apr">9.2</airtemp>
      <airtemp id="May">15.1</airtemp>
      <airtemp id="Jun">19.5</airtemp>
      <airtemp id="Jul">21.8</airtemp>
      <airtemp id="Aug">21.0</airtemp>
      <airtemp id="Sep">16.8</airtemp>
      <airtemp id="Oct">10.7</airtemp>
      <airtemp id="Nov">5.0</airtemp>
      <airtemp id="Dec">-0.3</airtemp>
    </airtemps>
    <smcsawc>200.0</smcsawc>
    <soilairrel>
      <ampltd>0.66</ampltd>
      <maatmast>1.2</maatmast>
    </soilairrel>
  </input>
  <output>
    <smrclass>Udic</smrclass>
    <strclass>Mesic</strclass>
    <subgrpmod />
    <awb>362.7</awb>
    <swb>-73.53</swb>
    <smcstates>
      <cumdays>
        <yrdry>0</yrdry>
        <yrmd>0</yrmd>
        <yrmst>360</yrmst>
        <bio5dry>0</bio5dry>
        <bio5md>0</bio5md>
        <bio5mst>221</bio5mst>
      </cumdays>
      <consdays>
        <yrmst>360</yrmst>
        <bio8mst>201</bio8mst>
        <smrdry>0</smrdry>
        <wtrmst>120</wtrmst>
      </consdays>
    </smcstates>
    <pets>
      <pet id="Jan">0.0</pet>
      <pet id="Feb">0.0</pet>
      <pet id="Mar">10.63</pet>
      <pet id="Apr">42.23</pet>
      <pet id="May">86.16</pet>
      <pet id="Jun">118.02</pet>
      <pet id="Jul">135.98</pet>
      <pet id="Aug">121.83</pet>
      <pet id="Sep">81.47</pet>
      <pet id="Oct">43.78</pet>
      <pet id="Nov">15.01</pet>
      <pet id="Dec">0.0</pet>
    </pets>
    <soiltemps>
      <soiltemp id="Jan">5.03</soiltemp>
      <soiltemp id="Feb">5.03</soiltemp>
      <soiltemp id="Mar">5.82</soiltemp>
      <soiltemp id="Apr">8.04</soiltemp>
      <soiltemp id="May">11.03</soiltemp>
      <soiltemp id="Jun">13.99</soiltemp>
      <soiltemp id="Jul">16.12</soiltemp>
      <soiltemp id="Aug">16.51</soiltemp>
      <soiltemp id="Sep">14.62</soiltemp>
      <soiltemp id="Oct">11.8</soiltemp>
      <soiltemp id="Nov">8.74</soiltemp>
      <soiltemp id="Dec">6.26</soiltemp>
    </soiltemps>
    <calendars>
      <tempcal>
        <stlt5>
        <beginday>1</beginday>
        <endday>104</endday>
        </stlt5>
        <st5to8>
        <beginday>105</beginday>
        <endday>113</endday>
        </st5to8>
        <stgt8>
        <beginday>114</beginday>
        <endday>314</endday>
        </stgt8>
        <st5to8>
        <beginday>315</beginday>
        <endday>325</endday>
        </st5to8>
        <stlt5>
        <beginday>326</beginday>
        <endday>360</endday>
        </stlt5>
      </tempcal>
      <moistcal>
        <moist>
        <beginday>1</beginday>
        <endday>360</endday>
        </moist>
      </moistcal>
    </calendars>
  </output>
</model>

# CSV File Format Structure

The classic CSV file format used by the BASIC version of Newhall is a simple file format which contains the bare minimum in order to run the model. It consists only of a station name, a country, degrees/minutes for a location, hemispheres, elevation, unit system, precipitation, temperature, and year(s).

The general structure follows the following pattern. White space is ignored by both the BASIC version and the Java version.

Station Name, Country, Degrees Latitude, Minutes Latitude, N/S Hemisphere, Degrees Longitude, Minutes Longitude, E/W Hemisphere, Elevation [NEWLINE]
Pre0, Pre1, Pre2, Pre3, Pre4, Pre5, Pre6, Pre7, Pre8, Pre9, Pre10, Pre11, Tmp0, Tmp1, Tmp2, Tmp3, Tmp4, Tmp5, Tmp6, Tmp7, Tmp8, Tmp9, Tmp10, Tmp11, Starting Year, Ending Year, Unit System [NEWLINE]
## Example Files

"Mead Agronomy Lab","USA",41,10,"N",96,25,"W",1180 [NEWLINE]
.8,.46,.06,.99,4.08,4.14,3.26,1.62,2.94,.85,.05,.66,32,15,37,55,63,69,76, 73,63,54,36,17,1989,1989,"E" [NEWLINE]

"Dickinson Expt Station ND","USA",46,53,"N",102,48,"W",2460 [NEWLINE]
.43 , .38 , .68 , 1.42 , 2.38 , 3.67 , 2.16 , 1.79 , 1.36 , .95 , .52 , .39 , 10.8 , 15 , 26.2 , 41.2 , 52.6 , 61.9 , 68.5 , 66.9 , 55.9 , 44.2 , 28.3 , 16.5 ,1903,1996,"E" [NEWLINE]

This manual and the Newhall executable should include several additional datasets. Refer to them yet more examples.
# License, Distribution, and Modification

This version of the Newhall model is released under the New BSD open-source license, also known as the “Three Clause BSD” license. The content of this license is available in the “About” dialog available in the “Help” menu inside Newhall, and also in the LICENSE file included with Newhall. This license effectively states that you agree to the following if you use this software:

1. You may do whatever you wish with this software, so long as you abide by all the following terms.
2. You will include or refer to all the original documents in any redistribution or derivative works. This includes the license file with copyright notice, this manual, and so forth. Simply stating “this version is based on the work of (parties), located at (software project website)” would be sufficient.
3. You may not use the names of the original authors and copyright holders as endorsement for any derivative products you may create with the source code of this program. You must explicitly seek the permission of the original authors to do this.

These stipulations are stated to preserve this software as an open-source entity, that can be shared for free and altered/extended/enhanced by anyone who wishes to do so. Copyright is only established to protect the original authors from retroactive intellectual property lawsuits, as would be possible by a public domain release.